VARIATION TO LICENCE AREA PLAN

Gold Coast Radio

Australian Broadcasting Authority
Canberra

April 2005

Commonwealth of Australia, April 2005

This work is copyright. Apart from fair dealings for the purpose of private study, research, criticism or review, as permitted by the Copyright Act 1968, no part may be reproduced or transmitted, in any form or by any means or process, without the written permission of the publishers.

Published by the Australian Broadcasting Authority
PO Box 34 
Belconnen  ACT  2616

VARIATION TO LICENCE AREA PLAN FOR GOLD COAST RADIO – No 1 of 2005

Pursuant to subsection 26(2) of the Broadcasting Services Act 1992, the Australian Broadcasting Authority varies the Licence Area Plan for Gold Coast Radio determined on 21 December 2000 (the principal instrument) in the manner set out below:

- The determination in the principal instrument is varied to:

(a) number each of the paragraphs in the determination consecutively as clauses (1) and (2);

(b) in clause (2):

(i) in line 1 omit the word “Four” and to substitute the word “Five”; and

(ii) omit the number “1.12” and substitute the number “1.13”.

(c) insert the following clause after clause (2):

“(3) A reference in this determination to a schedule or an attachment includes a reference to a schedule or attachment as amended from time to time”.

- Page 2 of the principal instrument is omitted

- Schedule One of the principal instrument is omitted and substituted with the table headed Schedule One in item 2 on page 3 of this instrument.

- Attachments to the principal instrument are varied to:

(a) omit Attachment 1.8 of the principal instrument and to substitute Attachment 1.8 of this instrument;

(b) omit Attachment 1.10 of the principal instrument and to substitute Attachment 1.10 of this instrument;

(c) omit Attachment 1.11 of the principal instrument and to substitute Attachment 1.11 of this instrument; and

(d) omit Attachment 1.12 of the principal instrument and to substitute Attachment 1.12 of this instrument.

- The instrument commences on the date of its determination by the Australian Broadcasting Authority.

The Common Seal of the 
Australian Broadcasting Authority
was affixed to this document
in the presence of:

Lyn Maddock					Robert Le Tet

Signature of Member				Signature of Member

Lyn Maddock					Robert Le Tet

Dated this 14th day of April 2005.

Variation to the Schedule to the Licence Area Plan for Gold Coast Radio

(Clause 3)

Item 1

Schedule One of the Licence Area Plan for Gold Coast Radio (as varied by the ABA on 27 February 2003) is reproduced in this item for ease of reference only.

Schedule One

Licence Area Plan: Gold Coast Radio - December 2000

Licence Area : GOLD COAST RA1

| Service Category | Status | Frequency | Service Licence No | Technical Specification No | Attach No | Area Served |
| --- | --- | --- | --- | --- | --- | --- |
| National | Licensed Reserved | 88.5 MHz | N/A | TS2138001 | 1.2 | Gold Coast |
| National | Licensed Reserved | 90.1 MHz | N/A | TS2139001 | 1.3 | Gold Coast |
| National | Licensed Reserved | 91.7 MHz | N/A | TS2268601 | 1.4 | Gold Coast |
| National | Licensed Reserved | 97.7 MHz | N/A | TS7329601 | 1.5 | Gold Coast |
| National | Licensed Reserved | 95.7 MHz | N/A | TS6252001 | 1.13 | Gold Coast |
| Commercial | Licensed | 90.9 MHz | SL3182 | TS3182001 | 1.6 | Gold Coast |
| Commercial | Licensed | 92.5 MHz | SL4173 | TS4173001 | 1.7 | Gold Coast |
| Commercial | Licensed | 102.9 MHz | SL1150463 | TS10012787 | 1.8.1 | Gold Coast |
| Community | Licensed | 89.3 MHz | SL3069 | TS3069001 | 1.9 | Gold Coast |
| Community | Licensed | 94.1 MHz | SL1150707 | TS10012788 | 1.10.1 | Gold Coast |
| Community | Licensed | 105.7 MHz | SL1150709 | TS10012789 | 1.11.1 | Gold Coast |
| Community | Licensed | 107.3 MHz | SL1150708 | TS10012790 | 1.12.1 | Gold Coast |

Item 2

The updated Schedule One to the Licence Area Plan for Gold Coast Radio as varied by this instrument is as follows:

Schedule One

Licence Area Plan: Gold Coast Radio

Licence Area : GOLD COAST RA1

| Service Category | Channel/ Frequency | Service Licence No | Transmitter Specification No | Attach No | Area Served |
| --- | --- | --- | --- | --- | --- |
| National | 88.5 MHz | N/A | TS2138001 | 1.2 | Gold Coast |
| National | 90.1 MHz | N/A | TS2139001 | 1.3 | Gold Coast |
| National | 91.7 MHz | N/A | TS2268601 | 1.4 | Gold Coast |
| National | 97.7 MHz | N/A | TS7329601 | 1.5 | Gold Coast |
| National | 95.7 MHz | N/A | TS6252001 | 1.13 | Gold Coast |
| Commercial | 90.9 MHz | SL3182 | TS3182001 | 1.6 | Gold Coast |
| Commercial | 92.5 MHz | SL4173 | TS4173001 | 1.7 | Gold Coast |
| Commercial | 102.9 MHz | SL1150463 | TS10013951 | 1.8 | Gold Coast |
| Community | 89.3 MHz | SL3069 | TS3069001 | 1.9 | Gold Coast |
| Community | 94.1 MHz | SL1150707 | TS10013952 | 1.10 | Gold Coast |
| Community | 105.7 MHz | SL1150709 | TS10013953 | 1.11 | Gold Coast |
| Community | 107.3 MHz | SL1150708 | TS10013954 | 1.12 | Gold Coast |

Attachment	1.8

LICENCE AREA PLAN: Gold Coast Radio

Category :	Commercial

General Area Served :	Gold Coast (QLD)

Service Licence Number :	SL1150463

TECHNICAL SPECIFICATION - FM Radio

Specification Number :	TS10013951

Transmitter Site :-

Nominal location :	Large Link Tower within Broadcast Enclosure  Golf Course Rd
MOUNT TAMBORINE

Australian Map Grid :	Zone	Easting	Northing
Reference	56	520880	6905960

Site Tolerance :	Refer to Technical Planning Guidelines

Emission :-

Frequency Band & Mode	VHF-FM

Carrier Frequency :	102.9 MHz

Polarisation	Mixed

Maximum antenna height	63 m

Output Radiation Pattern :-

| Bearing or Sector (Clockwise direction) | Maximum ERP |
| --- | --- |
| 0°T - 30°T | 2 kW |
| 30°T - 80°T | 16 kW |
| 80°T - 140°T | 25 kW |
| 140°T - 160°T | 16 kW |
| 160°T - 180°T | 10 kW |
| 180°T - 210°T | 3 kW |
| 210°T - 360°T | 250 W |

Attachment	1.10

LICENCE AREA PLAN: Gold Coast Radio

Category :	Community

General Area Served :	Gold Coast (QLD)

Service Licence Number :	SL1150707

TECHNICAL SPECIFICATION - FM Radio

Specification Number :	TS10013952

Transmitter Site :-

Nominal location :	Large Link Tower within Broadcast Enclosure Golf Course Rd
MOUNT TAMBORINE

Australian Map Grid :	Zone	Easting	Northing
Reference	56	520880	6905960

Site Tolerance :	Refer to Technical Planning Guidelines

Emission :-

Frequency Band & Mode	VHF-FM

Carrier Frequency :	94.1 MHz

Polarisation	Mixed

Maximum antenna height	63 m

Output Radiation Pattern :-

| Bearing or Sector (Clockwise direction) | Maximum ERP |
| --- | --- |
| 0°T - 30°T | 2 kW |
| 30°T - 80°T | 16 kW |
| 80°T - 140°T | 25 kW |
| 140°T - 160°T | 16 kW |
| 160°T - 180°T | 10 kW |
| 180°T - 210°T | 3 kW |
| 210°T - 360°T | 250 W |

Attachment	1.11

LICENCE AREA PLAN: Gold Coast Radio

Category :	Community

General Area Served :	Gold Coast (QLD)

Service Licence Number :	SL1150709

TECHNICAL SPECIFICATION - FM Radio

Specification Number :	TS10013953

Transmitter Site :-

Nominal location :	Large Link Tower within Broadcast Enclosure Golf Course Rd
MOUNT TAMBORINE

Australian Map Grid :	Zone	Easting	Northing
Reference	56	520880	6905960

Site Tolerance :	Refer to Technical Planning Guidelines

Emission :-

Frequency Band & Mode	VHF-FM

Carrier Frequency :	105.7 MHz

Polarisation	Mixed

Maximum antenna height	63 m

Output Radiation Pattern :-

| Bearing or Sector (Clockwise direction) | Maximum ERP |
| --- | --- |
| 0°T - 30°T | 800 W |
| 30°T - 80°T | 6.5 kW |
| 80°T - 140°T | 10 kW |
| 140°T - 160°T | 6.5 kW |
| 160°T - 180°T | 4 kW |
| 180°T - 210°T | 1.2 kW |
| 210°T - 360°T | 100 W |

Attachment	1.12

LICENCE AREA PLAN: Gold Coast Radio

Category :	Community

General Area Served :	Gold Coast (QLD)

Service Licence Number :	SL1150708

TECHNICAL SPECIFICATION - FM Radio

Specification Number :	TS10013954

Transmitter Site :-

Nominal location :	Large Link Tower within Broadcast Enclosure  Golf Course Rd
MOUNT TAMBORINE

Australian Map Grid :	Zone	Easting	Northing
Reference	56	520880	6905960

Site Tolerance :	Refer to Technical Planning Guidelines

Emission :-

Frequency Band & Mode	VHF-FM

Carrier Frequency :	107.3 MHz

Polarisation	Mixed

Maximum antenna height	63 m

Output Radiation Pattern :-

| Bearing or Sector (Clockwise direction) | Maximum ERP |
| --- | --- |
| 0°T - 30°T | 800 W |
| 30°T - 80°T | 6.5 kW |
| 80°T - 140°T | 10 kW |
| 140°T - 160°T | 6.5 kW |
| 160°T - 180°T | 4 kW |
| 180°T - 210°T | 1.2 kW |
| 210°T - 360°T | 100 W |