Instrument number CASA 374/11

I, GREGORY JAMES HOOD, Executive Manager, Operations Division, a delegate of CASA, make this instrument under regulation 208 of the Civil Aviation Regulations 1988.

[Signed Greg Hood]

Greg Hood
Executive Manager
Operations Division

24 August 2011

Direction — number of cabin attendants

1	Duration

This instrument:

(a)	commences on 1 September 2011; and

(b)	stops having effect at the end of 30 November 2011.

2	Application

This instrument applies to the aircraft mentioned in Schedule 1 operated by Jetstar Airways Pty Limited, Aviation Reference Number 510654 (the operator), and engaged in regular public transport operations.

3	Direction

In spite of subparagraph 6.1 (b) of Civil Aviation Order 20.16.3 (CAO 20.16.3), the operator may operate the aircraft if there is 1 cabin attendant for every 50 passenger seats or part of that number.

Note   CAO 20.16.3 applies in all other respects to the aircraft mentioned in Schedule 1.

4	Conditions

The direction is subject to the conditions mentioned in Schedule 2.

Schedule 1	Aircraft

Australian registered Airbus A321-200 series aircraft with a type certificate data sheet that provides for a maximum seating capacity of 220 passengers or an Australian registered Airbus A320-200 series aircraft with a type certificate data sheet that provides for a maximum seating capacity of 180 passengers.

Schedule 2	Conditions

1	Only physically competent (able-bodied) persons may occupy seats in the emergency exit rows.

2	During the aircraft take-off, landing operation and in prepared emergencies, emergency exit row seats must be occupied by a minimum of 2 physically competent (able-bodied) persons.

3	All passengers seated in the emergency exit rows must receive and respond to a briefing acceptable to CASA which instructs them on the operation of the emergency exits and subsequent actions required in the event of an emergency.

4	The operator must ensure that the aircraft can be evacuated in 90 seconds.

5	Arrangements for the seating and briefing of passengers must be in accordance with procedures set out in the operator’s operations manual and acceptable to CASA.