Instrument number CASA 506/11

I, GREGORY JAMES HOOD, Executive Manager, Operations Division, a delegate of CASA, make this instrument under regulation 208 of the Civil Aviation Regulations 1988.

[Signed Greg Hood]

Greg Hood 
Executive Manager
Operations Division

12 December 2011

Direction — number of cabin attendants (Sunstate Airlines)

1	Duration

This instrument:

(a)	commences on 1 January 2012; and

(b)	stops having effect at the end of 30 June 2012.

2	Application

This instrument applies to an aircraft mentioned in section 3 that is operated by Sunstate Airlines (Qld) Pty Limited, Aviation Reference Number 065667 (the operator), and engaged in regular public transport, or charter, operations.

3	Direction

In spite of subparagraph 6.1 (b) of Civil Aviation Order 20.16.3 (CAO 20.16.3), the operator may operate an Australian registered Dash 8-400 aircraft with a type certificate data sheet that provides for a maximum seating capacity of 78 passengers if there is 1 cabin attendant for every 50 passenger seats or part of that number.

Note   CAO 20.16.3 applies in all other respects to an aircraft referred to in this section.

4	Conditions

The direction is subject to the conditions mentioned in Schedule 1.

Schedule 1	Conditions

1	Only physically competent (able-bodied) persons may occupy row 2 right-hand seats.

2	During the aircraft take-off, landing operation and in prepared emergencies, whenever there are passengers on the aircraft, row 2 right-hand seats must be occupied by 2 physically competent (able-bodied) persons.

3	All passengers seated in row 2 right-hand side seats must receive and respond to a briefing approved by CASA which instructs them on the operation of emergency exits and subsequent actions required in the event of an emergency.

4	The operator must ensure that the aircraft can be evacuated in 90 seconds.

5	Arrangements for the seating and briefing of passengers must be in accordance with procedures set out in the operator’s operations manual and approved by CASA.

6	A copy of this direction must be included in the operator’s operations manual as made and without alteration.